Last time
Course mechanics
What is the Internet?
  - hosts, routers, communication links
  - communications services, protocols
Network Edge
  - client-server, peer-to-peer
  - TCP, UDP
Network Core
  - Circuit-switched networks
    - FDM
    - TDM
  - Packet-switched networks

---
This time
Finish introduction and overview:
  - Network access and physical media
  - Internet structure and ISPs
  - Delay & loss in packet-switched networks
  - Protocol layers, service models

---
Chapter 1: roadmap
  - 1.1 What is the Internet?
  - 1.2 Network edge
  - 1.3 Network core
  - 1.4 Network access and physical media
  - 1.5 Internet structure and ISPs
  - 1.6 Delay & loss in packet-switched networks
  - 1.7 Protocol layers, service models
  - 1.8 History

---
Access networks and physical media
Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?
latency?

---
Residential access: point to point access
Residential access: point to point access
Dialup via modem
  - up to 56 kbps direct access to router (often less)
  - Can’t surf and phone at same time: not “always on”
ADSL: asymmetric digital subscriber line
up to 1 Mbps upstream
up to 8 Mbps downstream
FDM: 200 kHz – 1 MHz for downstream
25 kHz – 160 kHz for upstream
0 kHz – 4 kHz for ordinary telephone

---
Residential access: cable modems
Residential access: cable modems
HFC: hybrid fiber coax
  - asymmetric: up to 30 Mbps downstream,
    2 Mbps upstream
Network of cable and fiber attaches homes to ISP router
  - homes share access to router
Deployment: available via cable TV companies

---
Company access: local area networks
Company access: local area networks
Company/univ local area network (LAN) connects end system to edge router
Ethernet:
  - shared or dedicated link connects end system and router
  - 10 Mbps, 100Mbps, Gigabit Ethernet
LANs: chapter 5

---
Wireless access networks
Wireless access networks
Shared wireless access network connects end system to router
  - via base station aka “access point”
Wireless LANs:
  - 802.11b/g (WiFi): 11 or 54 Mbps
  - This is what most laptops use to connect wirelessly.
  - Easy to set up your own base station.
base
station
mobile
hosts
router

---
Wireless access networks
Wider-area wireless access
  - Provided by telco operator
    - You can't set this up yourself
  - This is what cellphones use to connect wirelessly.
  - 2.5G: EDGE, GPRS, 1xRTT
    - 30 – 384 kbps
  - 3G: UMTS, 1xEV-DO
    - 144 kpbs – 2 Mbps
  - 3.5G: HSDPA
    - 10 Mbps
    - Rogers has been testing this in Toronto, and should be rolling it out commercially this Fall.
base
station
mobile
hosts
router

---
Home networks
Home networks
Typical home network components:
ADSL or cable modem
router/firewall/NAT
Ethernet
wireless access point
wireless
laptops
to/from
cable
headend
cable
modem
router/
firewall
wireless
access
point
Ethernet

---
Physical Media
Physical Media
Twisted Pair (TP)
Two insulated copper wires
  - Category 3: traditional phone wires, 10 Mbps Ethernet
  - Category 5:
    100 Mbps Ethernet
    1000 Mbps Ethernet
Physical link: what lies between transmitter & receiver
Guided media:
  - signals propagate in solid media: copper, fiber, coax
Unguided media:
  - signals propagate freely, e.g., radio

---
Physical Media: coax, fiber
Physical Media: coax, fiber
Fiber optic cable:
Glass fiber carrying light pulses, each pulse a bit
High-speed operation:
high-speed point-to-point transmission (e.g., 10’s-100’s Gbps)
Low error rate: repeaters spaced far apart; immune to electromagnetic noise
Coaxial cable:
Two concentric copper conductors
Baseband:
  - single channel on cable
  - legacy Ethernet
Broadband:
  - multiple channels on cable
  - HFC

---
Physical media: radio
Physical media: radio
Radio link types:
Terrestrial microwave
e.g. up to 45 Mbps channels
LAN (e.g., Wifi)
11Mbps, 54 Mbps
Wide-area (e.g., cellular)
e.g. 3G: hundreds of kbps
Satellite
240–270 msec end-to-end delay for geosynchronous
low altitude satellites?
Signal carried in electromagnetic spectrum
No physical “wire”
Propagation environment effects:
  - reflection
  - obstruction by objects
  - interference

---
Chapter 1: roadmap
  - 1.1 What is the Internet?
  - 1.2 Network edge
  - 1.3 Network core
  - 1.4 Network access and physical media
  - 1.5 Internet structure and ISPs
  - 1.6 Delay & loss in packet-switched networks
  - 1.7 Protocol layers, service models
  - 1.8 History

---
Internet structure: network of networks
Internet structure: network of networks
Roughly hierarchical
At center: “tier-1” ISPs (e.g., MCI, Sprint, AT&T, Cable and Wireless), national/international coverage
  - treat each other as equals
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
Tier 1 ISP
Tier 1 ISP
NAP
Tier-1 providers also interconnect at public network access points (NAPs)

---
Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  - Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
Tier-2 ISP is a customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other, interconnect at NAP

---
Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  - last hop (“access”) network (closest to end systems)
Local and tier-3 ISPs are customers of
higher tier ISPs
connecting them to the rest of the Internet
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

---
Internet structure: network of networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

---
Chapter 1: roadmap
  - 1.1 What is the Internet?
  - 1.2 Network edge
  - 1.3 Network core
  - 1.4 Network access and physical media
  - 1.5 Internet structure and ISPs
  - 1.6 Delay & loss in packet-switched networks
  - 1.7 Protocol layers, service models
  - 1.8 History

---
How do loss and delay occur?
How do loss and delay occur?
Packets queue in router buffers
Packet arrival rate to link exceeds output link capacity
Packets queue, wait for their turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

---
Four sources of packet delay
Four sources of packet delay
1. Processing delay:
check bit errors
determine output link
depends on processing power of router
2. Queueing delay:
time waiting at output link for transmissions
depends on congestion level of router
A
B
propagation
transmission
nodal
processing
queueing

---
Delay in packet-switched networks
Four sources of packet delay
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
Note: R and s are very different quantities!
 See UW-ACE for an applet comparing transmission and propagation delay.
A
B
propagation
transmission
nodal
processing
queueing

---
Nodal delay
Nodal delay
size 12{d rSub { size 8{"nodal"} } =d rSub { size 8{"proc"} } +d rSub { size 8{"queue"} } +d rSub { size 8{"trans"} } +d rSub { size 8{"prop"} } } {}
dproc = processing delay
  - typically a few microsecs or less
dqueue = queuing delay
  - depends on congestion
dtrans = transmission delay
  - = L/R, significant for low-speed links
dprop = propagation delay
  - a few microsecs to hundreds of msecs

---
Queueing delay (revisited)
Queueing delay (revisited)
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

---
“Real” Internet delays and routes
“Real” Internet delays and routes
What do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-to-end Internet path towards destination. For all i:
  - sends three packets that will reach router i on path towards destination
  - router i will return packets to sender
  - sender times interval between transmission and reply.
3 probes
3 probes
3 probes

---
“Real” Internet delays and routes
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
trans-oceanic
link
* means no response (probe lost, router not replying)

---
Packet loss
Packet loss
Queue (aka buffer) preceding link in buffer has finite capacity
When a packet arrives to a full queue, the packet is dropped (aka lost)
The lost packet may be retransmitted by previous node, by source end system, or not retransmitted at all
Other sources of loss?

---
Chapter 1: roadmap
  - 1.1 What is the Internet?
  - 1.2 Network edge
  - 1.3 Network core
  - 1.4 Network access and physical media
  - 1.5 Internet structure and ISPs
  - 1.6 Delay & loss in packet-switched networks
  - 1.7 Protocol layers, service models
  - 1.8 History

---
Protocol “Layers”
Protocol “Layers”
Networks are complex!
many “pieces”:
  - hosts
  - routers
  - links of various media
  - applications
  - protocols
  - hardware, software
Question:
Is there any hope of organizing the structure of networks?
Or at least our discussion of networks?

---
Internet protocol stack
Internet protocol stack
application: supporting network applications
  - FTP, SMTP, HTTP
transport: process-process data transfer
  - TCP, UDP
network: routing of datagrams from source to destination
  - IP, routing protocols
link: data transfer between neighboring network elements
  - PPP, Ethernet
physical: bits “on the wire”
application
transport
network
link
physical

---
Why layering?
Why layering?
Dealing with complex systems:
Explicit structure allows identification, relationship of complex system’s pieces
  - layered reference model for discussion
Modularization eases maintenance, updating of system
  - change of implementation of layer’s service transparent to rest of system
  - you probably saw similar things before (e.g. CS 350)

---
Encapsulation
Encapsulation
source
message
application
transport
network
link
physical
segment
datagram
frame
switch
destination
application
transport
network
link
physical
router
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
M
Ht
M
Ht
Hn
Hl
M

---
Chapter 1: roadmap
  - 1.1 What is the Internet?
  - 1.2 Network edge
  - 1.3 Network core
  - 1.4 Network access and physical media
  - 1.5 Internet structure and ISPs
  - 1.6 Delay & loss in packet-switched networks
  - 1.7 Protocol layers, service models
  - 1.8 History  Read on your own

---
Recap
Finished introduction and overview:
  - Network access and physical media
  - Internet structure and ISPs
  - Delay & loss in packet-switched networks
  - Protocol layers, service models

---
Next time
Start looking at the layers in turn
  - From physical layer up to application layer
Physical layer: already done
Next up: link layer
  - overview
  - error detection and correction
  - PPP