Last time
Router internals
  - Input ports, switching fabric, output ports
  - Switching via memory, bus, crossbar
  - Queueing, head-of-line blocking
Mobility
  - Home, visited networks
  - Home, foreign agents
  - Permanent, care-of addresses
  - Indirect vs. direct routing
Mobile IP
  - tunneling, agent discovery, registration

---
This time
Mobility in Cellular Networks
Transport layer
  - Introduction
  - Multiplexing
  - UDP

---
Components of cellular network architecture
Mobile
Switching
Center
Public telephone
network, and
Internet
Mobile
Switching
Center
connects cells to wide area net
manages call setup
handles mobility
MSC
covers geographical region
base station (BS) analogous to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network

---
Components of cellular network architecture
correspondent
wired public telephone
network
different cellular networks,
operated by different providers
MSC
MSC
MSC
MSC
MSC

---
Handling mobility in cellular networks
Handling mobility in cellular networks
Home network: network of cellular provider you subscribe to (e.g., Sprint PCS, Verizon)
  - home location register (HLR): database in home network containing permanent cell phone #, profile information (services, preferences, billing), information about current location (could be in another network)
Visited network: network in which mobile currently resides
  - visitor location register (VLR): database with entry for each user currently in network
  - could be home network

---
GSM: indirect routing to mobile
home
network
correspondent
Public switched
telephone
network
mobile
user
visited
network
home
Mobile
Switching
Center
HLR
Mobile
Switching
Center
VLR
1
call routed
to home network
2
home MSC consults HLR,
gets roaming number of
mobile in visited network
3
home MSC sets up 2nd leg of call
to MSC in visited network
4
MSC in visited network completes
call through base station to mobile

---
GSM: handoff with common MSC
Handoff goal: route call via new base station (without interruption)
Reasons for handoff:
  - stronger signal to/from new BSS (continuing connectivity, less battery drain)
  - load balance: free up channel in current BSS
  - GSM doesn’t mandate why to perform handoff (policy), only how (mechanism)
Handoff initiated by old BSS
new
routing
old
routing
old BSS
new BSS
Mobile
Switching
Center
VLR

---
GSM: handoff with common MSC
1. old BSS informs MSC of impending handoff, provides list of 1+ new BSSs
2. MSC sets up path (allocates resources) to new BSS
3. new BSS allocates radio channel for use by mobile
4. new BSS signals MSC, old BSS: ready
5. old BSS tells mobile: perform handoff to new BSS
6. mobile, new BSS signal to activate new channel
7. mobile signals via new BSS to MSC: handoff complete. MSC reroutes call
8 MSC-old-BSS resources released
old BSS
new BSS
Mobile
Switching
Center
VLR
1
3
2
4
5
6
7
8

---
GSM: handoff between MSCs
Anchor MSC: first MSC visited during call
  - call remains routed through anchor MSC
Anchor MSC sends call to current visited BSS
Always at most 3 hops
  - Home MSC
  - Anchor MSC
  - Visited MSC
correspondent
anchor MSC
PSTN
(a) before handoff
home network
Home MSC
MSC
MSC
MSC

---
GSM: handoff between MSCs
Anchor MSC: first MSC visited during call
  - call remains routed through anchor MSC
Anchor MSC sends call to current visited BSS
Always at most 3 hops
  - Home MSC
  - Anchor MSC
  - Visited MSC
correspondent
anchor MSC
PSTN
(b) after handoff
home network
Home MSC
MSC
MSC
MSC

---
Mobility: GSM versus Mobile IP
Mobility: GSM versus Mobile IP
Care-of-address
Routable address for telephone call segment between home MSC and visited MSC, visible to neither the mobile nor the correspondent.
Mobile Station Roaming Number (MSRN), or “roaming number”
Foreign agent
Visited MSC: responsible for setting up calls to/from mobile nodes in cells associated with MSC. VLR: temporary database entry in visited system, containing subscription information for each visiting mobile user
Visited Mobile services Switching Center.
Visitor Location Record (VLR)
Visited network
Network other than home system where mobile user is currently residing
Visited System
Home agent
Home MSC: point of contact to obtain routable address of mobile user. HLR: database in home system containing permanent phone number, profile information, current location of mobile user, subscription information
Gateway Mobile Switching Center, or “home MSC”. Home Location Register (HLR)
Home network
Network to which the mobile user’s permanent phone number belongs
Home system
Mobile IP element
Comment on GSM element
GSM element

---
Wireless, mobility: impact on higher layer protocols
Wireless, mobility: impact on higher layer protocols
Logically, impact should be minimal …
  - best effort service model remains unchanged
  - TCP and UDP can (and do) run over wireless, mobile
… but performance-wise:
  - packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handoff
  - TCP interprets loss as congestion, will decrease congestion window un-necessarily
  - delay impairments for real-time traffic
  - limited bandwidth of wireless links

---
Chapter 3: Transport Layer
Chapter 3: Transport Layer
Learn about transport layer protocols in the Internet:
  - UDP: connectionless transport
  - TCP: connection-oriented transport
  - TCP congestion control
Our goals:
Understand principles behind transport layer services:
  - multiplexing/
    demultiplexing
  - reliable data transfer
  - flow control
  - congestion control

---
Chapter 3 outline
Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  - segment structure
  - reliable data transfer
  - flow control
  - connection management
3.6 Principles of congestion control
3.7 TCP congestion control

---
Transport services and protocols
Transport services and protocols
Provide logical communication between app processes running on different hosts
Transport protocols run in end systems
  - sender side: breaks app messages into segments, passes to network layer
  - receiver side: reassembles segments into messages, passes to app layer
More than one transport protocol available to apps
  - Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

---
Transport vs. network layer
Transport vs. network layer
Household analogy:
12 kids sending letters to 12 kids
processes = kids
app messages = letters in envelopes
hosts = houses
transport protocol = Ann and Bill
network-layer protocol = postal service
Network layer: logical communication between hosts
Transport layer: logical communication between processes
  - relies on, enhances, network layer services

---
Internet transport-layer protocols
Internet transport-layer protocols
Reliable, in-order delivery (TCP)
  - congestion control
  - flow control
  - connection setup
Unreliable, unordered delivery: UDP
  - no-frills extension of “best-effort” IP
Services not available:
  - delay guarantees
  - bandwidth guarantees
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

---
Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  - segment structure
  - reliable data transfer
  - flow control
  - connection management
3.6 Principles of congestion control
3.7 TCP congestion control

---
Multiplexing/demultiplexing
Multiplexing/demultiplexing
delivering received segments
to correct socket
gathering data from multiple
sockets, enveloping data with
header (later used for
demultiplexing)
= socket
= process
application
P4
application
application
P1
P2
P3
P1
transport
transport
transport
network
network
network
link
link
link
physical
physical
physical
host 3
host 2
host 1
Demultiplexing at rcv host:
Multiplexing at send host:

---
How demultiplexing works
How demultiplexing works
Host receives IP datagrams
  - each datagram has source IP address, destination IP address
  - each datagram carries 1 transport-layer segment
  - each segment has source, destination port number
Host uses IP addresses & port numbers to direct segment to appropriate socket
32 bits
source port #
dest port #
other header fields
application
data
(message)
TCP/UDP segment format

---
Connectionless demultiplexing
Connectionless demultiplexing
When host receives UDP segment:
  - checks destination port number in segment
  - directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket
Create sockets with port numbers:
DatagramSocket mySocket1 = new DatagramSocket(12534);
DatagramSocket mySocket2 = new DatagramSocket(12535);
UDP socket identified by two-tuple:
(dest IP address, dest port number)

---
Connectionless demux (cont)
Connectionless demux (cont)
DatagramSocket serverSocket = new DatagramSocket(6428);
SP provides “return address”
Client
IP:B
P2
client
 IP: A
P1
P1
P3
server
IP: C
SP: 6428
DP: 9157
SP: 9157
DP: 6428
SP: 6428
DP: 5775
SP: 5775
DP: 6428

---
Connection-oriented demux
Connection-oriented demux
TCP socket identified by 4-tuple:
  - source IP address
  - source port number
  - dest IP address
  - dest port number
Recv host uses all four values to direct segment to appropriate socket
Server host may support many simultaneous TCP sockets:
  - each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client
  - non-persistent HTTP will have different socket for each request

---
Connection-oriented demux (cont)
Connection-oriented demux (cont)
S-IP: B
D-IP:C
SP: 9157
DP: 80
Client
IP:B
server
IP: C
S-IP: A
S-IP: B
D-IP:C
D-IP:C
P1
client
 IP: A
P1
P2
P4
SP: 9157
DP: 80
P5
P6
P3
SP: 5775
DP: 80

---
Connection-oriented demux: Threaded Web Server
Connection-oriented demux: Threaded Web Server
P4
S-IP: B
D-IP:C
SP: 9157
DP: 80
Client
IP:B
server
IP: C
S-IP: A
S-IP: B
D-IP:C
D-IP:C
P1
client
 IP: A
P1
P2
SP: 9157
DP: 80
P3
SP: 5775
DP: 80

---
Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  - segment structure
  - reliable data transfer
  - flow control
  - connection management
3.6 Principles of congestion control
3.7 TCP congestion control

---
UDP: User Datagram Protocol [RFC 768]
UDP: User Datagram Protocol [RFC 768]
“No frills,” “bare bones” Internet transport protocol
“Best effort” service; UDP segments may be:
  - lost
  - delivered out of order to app
Connectionless:
  - no handshaking between UDP sender, receiver
  - each UDP segment handled independently of others
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header
no congestion control: UDP can blast away as fast as desired

---
UDP: more
UDP: more
Often used for streaming multimedia apps
  - loss tolerant
  - rate sensitive
Other UDP uses
  - DNS
  - SNMP
Reliable transfer over UDP: add reliability at application layer
  - application-specific error recovery!
32 bits
source port #
dest port #
Length, in
bytes of UDP
segment,
including
header
checksum
length
Application
data
(message)
UDP segment format

---
UDP checksum
UDP checksum
Goal: detect “errors” (e.g., flipped bits) in transmitted segment
Receiver:
test checksum of received segment
  - accept or discard segment
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field

---
Recap
Mobility in Cellular networks
  - HLR, VLR, MSC
  - Handoff
Transport Layer
  - Introduction
  - Multiplexing / demultiplexing
  - UDP

---
Next time
Reliable Data Transfer
Midterm review