Last time
UDP socket programming
  - DatagramSocket, DatagramPacket
TCP
  - Sequence numbers, ACKs
  - RTT, DevRTT, timeout calculations
  - Reliable data transfer algorithm

---
This time
TCP
  - Fast retransmit
  - Flow control
  - Connection management
  - Congestion control

---
Fast  Retransmit
Fast Retransmit
Time-out period often relatively long:
  - long delay before resending lost packet
Detect lost segments via duplicate ACKs.
  - Sender often sends many segments back-to-back
  - If segment is lost, there will likely be many duplicate ACKs.
If sender receives 3 ACKs for the same data, it supposes that segment after ACKed data was lost:
  - fast retransmit: resend segment before timer expires

---
Fast retransmit algorithm:
Fast retransmit algorithm:
 event: ACK received, with ACK field value of y
        if (y > SendBase) {
        SendBase = y
        if (there are currently not-yet-acknowledged segments)
        start timer
        }
        else {
        increment count of dup ACKs received for y
        if (count of dup ACKs received for y == 3) {
        resend segment with sequence number y
        }
a duplicate ACK for
already ACKed segment
fast retransmit

---
Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  - segment structure
  - reliable data transfer
  - flow control
  - connection management
3.6 Principles of congestion control
3.7 TCP congestion control

---
TCP Flow Control
TCP Flow Control
Receive side of TCP connection has a receive buffer:
Speed-matching service: matching the send rate to the receiving app’s drain rate
App process may be slow at reading from buffer
sender won’t overflow
receiver’s buffer by
transmitting too much,
 too fast
flow control

---
TCP Flow control: how it works
TCP Flow control: how it works
Rcvr advertises spare room by including value of RcvWindow in segments
Sender limits unACKed data to RcvWindow
  - guarantees receive buffer doesn’t overflow
See the applet in UW-ACE!
(Suppose TCP receiver discards out-of-order segments)
spare room in buffer
= RcvWindow
= RcvBuffer-[LastByteRcvd - LastByteRead]

---
Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  - segment structure
  - reliable data transfer
  - flow control
  - connection management
3.6 Principles of congestion control
3.7 TCP congestion control

---
TCP Connection Management
TCP Connection Management
Three way handshake:
Step 1: client host sends TCP SYN segment to server
  - specifies initial seq #
  - no data
Step 2: server host receives SYN, replies with SYNACK segment
  - server allocates buffers
  - specifies server initial seq. #
Step 3: client receives SYNACK, replies with ACK segment, which may contain data
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
  - seq. #s
  - buffers, flow control info (e.g. RcvWindow)
client: connection initiator
Socket clientSocket = new Socket("hostname","port number");
server: contacted by client
Socket connectionSocket = welcomeSocket.accept();

---
TCP Connection Management (cont.)
TCP Connection Management (cont.)
Closing a connection:
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server.
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait

---
TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
  - Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
Note: with small modification, can handle simultaneous FINs.
client
server
closing
closing
closed
closed
FIN
ACK
ACK
FIN
timed wait

---
TCP Connection Management (cont)
TCP Connection Management (cont)
TCP server
lifecycle
TCP client
lifecycle

---
Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  - segment structure
  - reliable data transfer
  - flow control
  - connection management
3.6 Principles of congestion control
3.7 TCP congestion control

---
Principles of Congestion Control
Principles of Congestion Control
Congestion:
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
  - lost packets (buffer overflow at routers)
  - long delays (queueing in router buffers)
a top-10 problem!

---
Causes/costs of congestion: scenario 1
Causes/costs of congestion: scenario 1
Two senders, two receivers
One router, infinite buffers
No retransmission
Large delays when congested
Maximum achievable throughput
unlimited shared output link buffers
Host A
in : original data
Host B
out

---
Causes/costs of congestion: scenario 2
Causes/costs of congestion: scenario 2
One router, finite buffers
Sender retransmission of lost packet
Host A
out
in : original data
'in : original data, plus retransmitted data
Host B
finite shared output link buffers

---
Causes/costs of congestion: scenario 2
Always: (goodput)
“Perfect” retransmission only when loss:
Retransmission of delayed (not lost) packet makes larger (than perfect case) for same
“Costs” of congestion:
More work (retransmissions) for given “goodput”
Unneeded retransmissions: link carries multiple copies of packet

in

out
=

in

out
>

in

out
R/2
R/2
in
out
b.
R/2
R/2
in
out
a.
R/2
R/2
in
out
c.
R/4
R/3

---
Causes/costs of congestion: scenario 3
Causes/costs of congestion: scenario 3
Four senders
Multihop paths
Timeout/retransmit
Q: what happens as and increase ?
out
in : original data
'in : original data, plus retransmitted data
finite shared output link buffers

in

in
Host A
Host B

---
Causes/costs of congestion: scenario 3
out
Another “cost” of congestion:
When packet dropped, any upstream transmission capacity used for that packet was wasted!
Host A
Host B

---
Approaches towards congestion control
Approaches towards congestion control
Two broad approaches towards congestion control:
Network-assisted congestion control:
routers provide feedback to end systems
  - single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  - explicit rate sender should send at
End-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP

---
Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  - segment structure
  - reliable data transfer
  - flow control
  - connection management
3.6 Principles of congestion control
3.7 TCP congestion control

---
TCP Congestion Control: details
TCP Congestion Control: details
Sender limits transmission:
LastByteSent-LastByteAcked
 CongWin
Roughly,
CongWin is dynamic, function of perceived network congestion
How does sender perceive congestion?
Loss event = timeout or 3 duplicate acks
TCP sender reduces rate (CongWin) after loss event
three mechanisms:
  - AIMD
  - slow start
  - conservative after timeout events
rate =
CongWin
RTT
Bytes/sec

---
TCP congestion control: additive increase, multiplicative decrease
TCP congestion control: additive increase, multiplicative decrease
Approach: increase transmission rate (window size), probing for usable bandwidth, until loss occurs
additive increase: increase CongWin by 1 MSS every RTT until loss detected
multiplicative decrease: cut CongWin in half after loss
Saw tooth
behavior: probing
for bandwidth
time
congestion window size

---
TCP Slow Start
TCP Slow Start
When connection begins, CongWin = 1 MSS
  - Example: MSS = 1 kBytes & RTT = 200 msec
  - initial rate = 40 kbps
available bandwidth may be >> MSS/RTT
  - desirable to quickly ramp up to respectable rate
When connection begins, increase rate exponentially fast until first loss event

---
TCP Slow Start (more)
TCP Slow Start (more)
When connection begins, increase rate exponentially until first loss event:
  - double CongWin every RTT
  - done by incrementing CongWin for every ACK received
Summary: initial rate is slow but ramps up exponentially fast
Host A
Host B
one segment
RTT
time
two segments
four segments

---
Refinement
Refinement
Q: When should the exponential increase switch to linear?
A: When CongWin gets to 1/2 of its value before timeout.
Implementation:
Variable Threshold
At loss event, Threshold is set to 1/2 of CongWin just before loss event

---
Refinement: inferring loss
Refinement: inferring loss
After 3 dup ACKs:
  - CongWin is cut in half
  - window then grows linearly
But after timeout event:
  - CongWin instead set to 1 MSS;
  - window then grows exponentially
  - to a threshold, then grows linearly
Philosophy:
3 dup ACKs indicates
network capable of
delivering some segments
Timeout indicates a “more alarming” congestion scenario

---
Summary: TCP Congestion Control
Summary: TCP Congestion Control
When CongWin is below Threshold, sender in slow-start phase, window grows exponentially.
When CongWin is above Threshold, sender is in congestion-avoidance phase, window grows linearly.
When a triple duplicate ACK occurs, Threshold set to CongWin/2 and CongWin set to Threshold.
When timeout occurs, Threshold set to CongWin/2 and CongWin is set to 1 MSS.

---
TCP sender congestion control
TCP sender congestion control
SS or CA
SS or CA
SS or CA
Congestion
Avoidance (CA)
Slow Start (SS)
State
CongWin and Threshold not changed
Increment duplicate ACK count for segment being acked
Duplicate ACK
Enter slow start
Threshold = CongWin/2,
CongWin = 1 MSS,
Set state to “Slow Start”
Timeout
Fast recovery, implementing multiplicative decrease. CongWin will not drop below 1 MSS.
Threshold = CongWin/2,
CongWin = Threshold,
Set state to “Congestion Avoidance”
Loss event detected by triple duplicate ACK
Additive increase, resulting in increase of CongWin by 1 MSS every RTT
CongWin = CongWin+MSS * (MSS/CongWin)
ACK receipt for previously unacked data
Resulting in a doubling of CongWin every RTT
CongWin = CongWin + MSS,
If (CongWin > Threshold)
      set state to “Congestion Avoidance”
ACK receipt for previously unacked data
Commentary
TCP Sender Action
Event

---
Recap
Fast retransmit
  - 3 duplicate ACKs
Flow control
  - Receiver windows
Connection management
  - SYN/SYNACK/ACK, FIN/ACK, TCP states
Congestion control
  - General concepts
TCP congestion control
  - AIMD, slow start, congestion avoidance

---
Next time
TCP
  - Throughput
  - Fairness
  - Delay modeling
TCP socket programming
NAT