Last time
Fast retransmit
  - 3 duplicate ACKs
Flow control
  - Receiver windows
Connection management
  - SYN/SYNACK/ACK, FIN/ACK, TCP states
Congestion control
  - General concepts
TCP congestion control
  - AIMD, slow start, congestion avoidance

---
This time
TCP
  - Throughput
  - Fairness
  - Delay modeling
TCP socket programming

---
TCP sender congestion control
TCP sender congestion control
SS or CA
SS or CA
SS or CA
Congestion
Avoidance (CA)
Slow Start (SS)
State
CongWin and Threshold not changed
Increment duplicate ACK count for segment being acked
Duplicate ACK
Enter slow start
Threshold = CongWin/2,
CongWin = 1 MSS,
Set state to “Slow Start”
Timeout
Fast recovery, implementing multiplicative decrease. CongWin will not drop below 1 MSS.
Threshold = CongWin/2,
CongWin = Threshold,
Set state to “Congestion Avoidance”
Loss event detected by triple duplicate ACK
Additive increase, resulting in increase of CongWin by 1 MSS every RTT
CongWin = CongWin+MSS * (MSS/CongWin)
ACK receipt for previously unacked data
Resulting in a doubling of CongWin every RTT
CongWin = CongWin + MSS,
If (CongWin > Threshold)
      set state to “Congestion Avoidance”
ACK receipt for previously unacked data
Commentary
TCP Sender Action
Event

---
TCP throughput
TCP Throughput
What’s the average throughout of TCP as a function of window size and RTT?
  - Ignore slow start
Let W be the window size when loss occurs.
When window is W, throughput is W/RTT
Just after loss, window drops to W/2, throughput to W/2RTT.
Average throughout: .75 W/RTT

---
TCP Futures: TCP over “long, fat pipes”
TCP Futures: TCP over “long, fat pipes”
Example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
Requires window size W = 83,333 in-flight segments
Throughput in terms of loss rate:
➜ L = 2·10-10 Wow
New versions of TCP for high-speed needed!
size 12{ { {1 "." "22" cdot ital "MSS"} over { ital "RTT" sqrt {L} } } } {}

---
TCP Fairness
TCP Fairness
Fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP
connection 2

---
Why is TCP fair?
Why is TCP fair?
Two competing sessions:
Additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
equal bandwidth share
R
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
Connection 1 throughput
R
Connection 2 throughput

---
Fairness (more)
Fairness (more)
Fairness and parallel TCP connections
Nothing prevents app from opening parallel connections between 2 hosts.
Web browsers do this
Example: link of rate R supporting 9 connections;
  - new app asks for 1 TCP, gets rate R/10
  - new app asks for 11 TCPs, gets R/2 !
Fairness and UDP
Multimedia apps often do not use TCP
  - do not want rate throttled by congestion control
Instead use UDP:
  - pump audio/video at constant rate, tolerate packet loss
Research area: TCP friendly

---
Delay modeling
Delay modeling
Notation, assumptions:
Assume one link between client and server of rate R
S: MSS (bits)
O: object size (bits)
no retransmissions (no loss, no corruption)
Window size:
First assume: fixed congestion window, W segments
Then dynamic window, modeling slow start
Q: How long does it take to receive an object from a Web server after sending a request?
Ignoring congestion, delay is influenced by:
TCP connection establishment
data transmission delay
slow start

---
Fixed congestion window (1)
Fixed congestion window (1)
First case:
WS/R > RTT + S/R: ACK for first segment in window returns before window’s worth of data sent
delay = 2RTT + O/R

---
Fixed congestion window (2)
Fixed congestion window (2)
Second case:
WS/R < RTT + S/R: wait for ACK after sending window’s worth of data sent
delay = 2RTT + O/R
+ (K-1)[S/R + RTT - WS/R]

---
TCP Delay Modeling: Slow Start (1)
TCP Delay Modeling: Slow Start (1)
Now suppose window grows according to slow start
Will show that the delay for one object is:
size 12{ ital "Latency"=2 ital "RTT"+ { {O} over {R} } +P left [ ital "RTT"+ { {S} over {R} } right ] - \( 2 rSup { size 8{P} } - 1 \) { {S} over {R} } } {}
where P is the number of times TCP idles at server:
size 12{P="min" lbrace Q,K - 1 rbrace } {}
- where Q is the number of times the server idles
   if the object were of infinite size.
- and K is the number of windows that cover the object.

---
TCP Delay Modeling: Slow Start (2)
TCP Delay Modeling: Slow Start (2)
Delay components:
2 RTT for connection estab and request
O/R to transmit object
time server idles due to slow start
Server idles:
P = min{K-1,Q} times
Example:
O/S = 15 segments
K = 4 windows
Q = 2
P = min{K-1,Q} = 2
Server idles P=2 times

---
TCP Delay Modeling (3)
TCP Delay Modeling (3)
alignl { stack { size 12{ { {S} over {R} } + ital "RTT"="time from when server starts to send segment "} {} # size 12{" until server receives acknowledgement"} {} } } {}
size 12{2 rSup { size 8{k - 1} } { {S} over {R} } ="time to transmit the kth window "} {}
size 12{ left [ { {S} over {R} } + ital "RTT" - 2 rSup { size 8{k - 1} } { {S} over {R} } right ] rSup { size 8{+{}} } =" idle time after the "k"th window"} {}
alignl { stack { size 12{"delay"= { {O} over {R} } +2 ital "RTT"+ Sum cSub { size 8{p=1} } cSup { size 8{P} } { ital "idleTime" rSub { size 8{p} } } } {} # = { {O} over {R} } +2 ital "RTT"+ Sum cSub { size 8{k=1} } cSup { size 8{P} } { \[ { {S} over {R} } } + ital "RTT" - 2 rSup { size 8{k - 1} } { {S} over {R} } \] {} # = { {O} over {R} } +2 ital "RTT"+P \[ ital "RTT"+ { {S} over {R} } \] - \( 2 rSup { size 8{P} } - 1 \) { {S} over {R} } {} } } {}

---
TCP Delay Modeling (4)
TCP Delay Modeling (4)
Recall K = number of windows that cover object
How do we calculate K ?
alignl { stack { size 12{K="min" lbrace k:2 rSup { size 8{0} } S+2 rSup { size 8{1} } S+ dotsaxis +2 rSup { size 8{k - 1} } S >= O rbrace } {} # ="min" lbrace k:2 rSup { size 8{0} } +2 rSup { size 8{1} } + dotsaxis +2 rSup { size 8{k - 1} } >= O/S rbrace {} # ="min" lbrace k:2 rSup { size 8{k} } - 1 >= { {O} over {S} } rbrace {} # ="min" lbrace k:k >= "log" rSub { size 8{2} } \( { {O} over {S} } +1 \) rbrace {} # = lceil "log" rSub { size 8{2} } \( { {O} over {S} } +1 \) rceil {} } } {}
Calculation of Q, number of idles for infinite-size object,
is similar (see text).

---
Chapter 2: Application layer
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
  - SMTP, POP3, IMAP
2.5 DNS
2.6 P2P file sharing
2.7 Socket programming with TCP
2.8 Socket programming with UDP
2.9 Building a Web server

---
Socket-programming using TCP
Socket-programming using TCP
Socket: a door between application process and end-end-transport protocol (UCP or TCP)
TCP service: reliable transfer of bytes from one process to another
controlled by
application
developer
controlled by
application
developer
controlled by
operating
system
controlled by
operating
system
internet
host or
server
host or
server
process
TCP with
buffers,
variables
socket
process
TCP with
buffers,
variables
socket

---
Socket programming with TCP
Socket programming with TCP
Client must contact server
server process must first be running
server must have created socket that welcomes client’s contact
Client contacts server by:
creating client-local TCP socket
specifying IP address, port number of server process
When client creates socket: client TCP establishes connection to server TCP
When contacted by client, server TCP creates new socket for server process to communicate with client
  - allows server to talk with multiple clients
  - source port numbers used to distinguish clients
TCP provides reliable, in-order
 transfer of bytes (“pipe”)
between client and server
application viewpoint

---
Client/server socket interaction: TCP
Client/server socket interaction: TCP
Server (running on hostid)
Client
wait for incoming
connection request
connectionSocket =
welcomeSocket.accept()
create socket,
port=x, for
incoming request:
welcomeSocket =
ServerSocket(x)
create socket,
connect to hostid, port=x
clientSocket = Socket(hostid, x)
close
connectionSocket
read reply from
clientSocket
close
clientSocket
send request using
clientSocket
read request from
connectionSocket
write reply to
connectionSocket
TCP
connection setup

---
Stream jargon
A stream is a sequence of characters that flow into or out of a process.
An input stream is attached to some input source for the process, e.g., keyboard or socket.
An output stream is attached to an output source, e.g., monitor or socket.
Client
process
client TCP socket

---
Socket programming with TCP
Example client-server app:
1) client reads line from standard input (inFromUser stream) , sends to server via socket (outToServer stream)
2) server reads line from socket
3) server converts line to uppercase, sends back to client
4) client reads, prints modified line from socket (inFromServer stream)

---
Example: Java client (TCP)
Example: Java client (TCP)
import java.io.*;
import java.net.*;
class TCPClient {
    public static void main(String argv[]) throws Exception
    {
        String sentence;
        String modifiedSentence;
        BufferedReader inFromUser =
        new BufferedReader(new InputStreamReader(System.in));
        Socket clientSocket = new Socket("hostname", 6789);
        DataOutputStream outToServer =
        new DataOutputStream(clientSocket.getOutputStream());
Create
input stream
Create
client socket,
connect to server
Create
output stream
attached to socket

---
Example: Java client (TCP), cont.
Example: Java client (TCP), cont.
Create
input stream
attached to socket
        BufferedReader inFromServer =
        new BufferedReader(new
        InputStreamReader(clientSocket.getInputStream()));
        sentence = inFromUser.readLine();
        outToServer.writeBytes(sentence + '\n');
        modifiedSentence = inFromServer.readLine();
        System.out.println("FROM SERVER: " + modifiedSentence);
        clientSocket.close();
    }
}
Send line
to server
Read line
from server

---
Example: Java server (TCP)
Example: Java server (TCP)
import java.io.*;
import java.net.*;
class TCPServer {
  public static void main(String argv[]) throws Exception
    {
      String clientSentence;
      String capitalizedSentence;
      ServerSocket welcomeSocket = new ServerSocket(6789);
      while(true) {
        Socket connectionSocket = welcomeSocket.accept();
        BufferedReader inFromClient =
        new BufferedReader(new
        InputStreamReader(connectionSocket.getInputStream()));
Create
welcoming socket
at port 6789
Wait, on welcoming
socket for contact
by client
Create input
stream, attached
to socket

---
Example: Java server (TCP), cont
Example: Java server (TCP), cont
        DataOutputStream outToClient =
        new DataOutputStream(connectionSocket.getOutputStream());
        clientSentence = inFromClient.readLine();
        capitalizedSentence = clientSentence.toUpperCase() + '\n';
        outToClient.writeBytes(capitalizedSentence);
        connectionSocket.close();
        }
    }
}
Create output
stream, attached
to socket
Read in line
from socket
Write out line
to socket
End of while loop,
loop back and wait for
another client connection

---
Recap
TCP
  - Throughput
  - Fairness
  - Delay modeling
TCP socket programming

---
Next time
NAT
Application layer
  - Intro
  - Web / HTTP